## Slide 1: Interfacing between Jetson Nano and Arduino
Advanced Research Computing Technology and Innovation Core
(ARCTIC)
Web: https://arctic.gsu.edu Email: arc@gsu.edu Slack: gsu-hpc.slack.com

## Slide 2: Jetson Nano
Single Board Computer
  Quad-core ARM A57 @ 1.43 GHz
  4 GB 64-bit LPDDR4 25.6 GB/s
  128-core Maxwell
Arduino
  Microcontroller
  Pyserial

## Slide 3: Options to connect
Option 1:
  Connect Jetson directly to I/O pins on Arduino and code everything in C
Option 2:
  Piggyback with App controls and send the JSON over the serial port

## Slide 4: PySerial
Python library to interface with the serial port (USB in our case)
Documentation at https://pyserial.readthedocs.io
Allows us to create a serial connection and interact using a class and methods

## Slide 5: How to use
Instantiate the serial class
baudrate (determined in serial.begin(int) of Arduino)
port (/dev/ttyUSB0 on jetson)
timeout (short)

## Slide 6: Read/Write Buffers
Everything that the Arduino prints will sit in the input buffer
you can check length via
  serial.in_waiting
    this returns the number of bytes in the buffer
  serial.out_waiting
    checks write buffer
    this means the Arduino is waiting to process commands from jetson

## Slide 7: Read/Write to serial port
Call serial.write
  must be a ascii byte encoded string
serial.readline()
  returns a single line
serial.readall()
  reads the entire buffer

## Slide 8: Interfacing with Arduino
Uses json with specific parameters to call the motor changes from yesterday
Movement is
  {N: 102, D1: int for direction, D2: speed}
Forward at 100 speed
  {N: 102, D1: 4, D2: 100}

## Slide 9: serial_car_control.py
Providing a wrapper that gives simple easy commands to control car

## Slide 10: To the code…